## Slide 1
Tishk International University
Engineering Faculty
Interior Design Department
Criteria of Interior Design
4th Grade- Spring Semester 2024-2025
TOPIC: Estimation of Stone,
Cement Mortar & Concrete Mixing
Instructor: Barham Haidar Ali

## Slide 2: Ch5. Estimation of quantities in engineering projects
Estimation is one of the main factors in predicting the cost of the projects.
Types of estimate:
Approximate Estimate.
Quantity Estimate.
Detailed Estimate.
Supplementary Estimate.
Revised Estimate.
1. Approximate Estimate:
Quantities are approximately estimated according to dimensions like;
Square meters.
Cubic meters.

## Slide 3
2. Quantity Estimate (Estimating of Quantities of materials):
1- Bricks:
Size of Brick as illustrated in the figure is (7*11*23)cm3.
Joint thickness (cement mortar 1:3) = 1.0 cm.
If the width of the wall is 36cm or more:
  Size of Brick will be (8*12*24)cm3
Brick
23cm
7cm
11cm
Number of bricks in 1m3 of brick masonry work =
other approximations also used but most accurate is 435.
If the width of the wall is 24cm:
Number of bricks in 1m3 of brick masonry work =
If the width of the wall is 12cm:
Number of bricks in 1m2 of brick masonry work =
If the width of the wall is 8cm:
Number of bricks in 1m2 of brick masonry work =

## Slide 4
Example: find the number of bricks for the following wall for thickness; 40cm, 24cm, 12cm and 8cm.
1
2.2
1.4
1.6
6
3.5

## Slide 5
2- concrete Blocks:
Size of Blocks as illustrated in the figure is:
(20*20*40)cm3 (Hollow type)
(15*20*40)cm3 (Solid type)
(10-12*20*40)cm3 (Hollow type)
Joint thickness (cement mortar 1:3) = 2.5 to 3.0 cm.(use 3cm)
If the width of the wall is 20cm :
  Size of Block will be (20*23*43)cm3
40
20
20
Hollow
Solid
40
15
20
Number of blocks in 1m3 =
If the width of the wall is 40cm:
  Size of Block will be (23*23*40)cm3
Number of blocks in 1m3 =

## Slide 6
If the width of the wall is 12cm :
Number of blocks in 1m3 =
If quantities of block required in m2 of wall;
- If the width of the wall is 20cm :
Number of blocks in 1m2 =
- If the width of the wall is 12cm :
Number of blocks in 1m2 =
Example: find amount of block required in (m2 and m3) to build the following wall, if the thickness of wall is; 20cm, 40cm, or 12cm.
2.2
0.8
1
5
2
2.2
4
1
isometric

## Slide 7
3- Stones:
If the Size of Stones is (30cm*30cm)
Joint thickness (cement mortar 1:3) = 3.0 cm
If the width of the wall is 30cm or 40cm :
Number of stones in 1m2 =
But for each side of the wall requires (9.2) as illustrated in sketch
For both side of the wall
Wall thickness
30 or 40cm
30 cm
3 cm
Sectional Top view of stone wall

## Slide 8
4- Cement, Sand and Gravel:
Cement mortar in Brick works:
Volume of Bricks in 1m3 of brick work = volume of one Brick * Number of Bricks
= (0.07 * 0.11 * 0.23) * 435
= 0.77 m3
Volume of Mortar in 1m3 of brick work = 1 - 0.77 = 0.23 m3
Then, Cement (C) and Sand (S) quantities can be calculated as follows:
if C : S equal to 1 : 3, means: C=1, S=3
V= 0.75 (C+S) , when V=0.23m3 as obtained before;
0.23=0.75 (C+3C) C = 0.077 m3 , S = 3 * 0.077 = 0.231 m3
Each 1m3 of cement = 1400 kg
The weight of cement = 0.077 * 1400 = 107.8 kg
Cement and Sand quantities in 1m2 of Cement Plastering:
Thickness of plastering = 2 cm
Volume of cement mortar in 1m2 of plastering = 0.02 * 1 = 0.02 m3
0.02=0.75 (C+3C) C = 0.0067 m3 , S = 3 * 0.0067 = 0.0201 m3
The weight of cement = 0.0067 * 1400 = 9.4 kg
V = 0.75 ( C + S )

## Slide 9
Cement, Sand, and Gravel in concrete mixes:
Cement (C), Sand (S), and Gravel (G) quantities can be calculated as follows:
if proportion is (C : S : G) equal to (1 : 2 : 4) , means: C=1, S=2, and G=4
V= 0.67 (C+S+G) , when V=1m3 of Mixed material;
1=0.67(C+2C+4C) C = 0.213 m3 ,
S = 2 * 0.213 = 0.426 m3
G = 4 * 0.213 = 0.852 m3
The weight of cement = 0.213 * 1400 = 298.2 kg ≈ 300 kg
V = 0.67 ( C + S + G )
if proportion is (C : S : G) equal to (1 : 1.5 : 3) , means: C=1, S=1.5, and G=3
V= 0.67 (C+S+G) , when V=1m3 of Mixed material;
1=0.67(C+1.5C+3C) C = 0.271 m3 ,
S = 1.5 * 0.271 = 0.4065 m3
G = 3 * 0.271 = 0.813 m3
The weight of cement = 0.271 * 1400 = 379.4 kg ≈ 380 kg
if proportion is (C : S : G) equal to (1 : 4 : 8)
V= 0.67 (C+S+G) , when V=1m3 of Mixed material;
1=0.67(C+4C+8C) C = 0.115 m3 ,
S = 4 * 0.115 = 0.46 m3
G =8 * 0.115 = 0.92 m3
The weight of cement = 0.115 * 1400 = 161 kg

## Slide 10
5- Tiles:
Glass Tile; if size 15cm * 15cm :
Joint= 3.0 mm
Number of Tiles in 1m2 =
If size 20cm * 25cm :
Number of Tiles in 1m2 =
Floor Tiles; if size 30cm * 30cm :
Number of Tiles in 1m2 =
If size 40cm * 40cm :
Number of Tiles in 1m2 =
If size 50cm * 50cm :
Number of Tiles in 1m2 =

## Slide 11
6- Reinforced Steel:
Straight bars:
22 | 20 | 16 | 12 | 10 | d=ф
2.987 | 2.469 | 1.58 | 0.888 | 0.617 | Kg/m
7/8 | 6/8 | 5/8 | 4/8 | 3/8 | in
28 | 34 | 53 | 93 | 135 | 12mBar/ton
Bent bars:
L
k
k
L
k
k
(L+2K)
l
l
1.42d
(L+2K+2l+2.84d)
Example: For the following reinforcement plan, estimate the quantity of the steel required.
S1 (3*5)
S2
S3
S4
S1
a
b
c
d
e
Where; a= ф12@25c/c
b= ф12@25c/c c= ф10@30c/c
d= ф10@30c/c e= ф10@30c/c (1.5m)
Slab:

## Slide 12
Main bars (in short span):
  Straight bars:
  length=4-0.04 = 3.96
    Number of bars
  Bent bars:
  length=(4-0.04)+0.84d
  = 3.96+0.84*0.11=4.052m
    Number of bars
21 No. Φ12 with length of 3.96m
21 No. Φ12 with length of 4.05m

## Slide 13
  Additional bars:
  length=1.5m
    Number of bars
Secondary bars (Long Span):
  Straight bars:
  length=5-0.04 = 4.96
    Number of bars
15 No. Φ10 with length of 4.96m
36 No. Φ10 with length of 1.5m
  Bent bars:
  length=(5-0.04)+0.84d
  = 3.96+0.84*0.11=5.052m
    Number of bars
15 No. Φ10 with length of 5.05m

## Slide 14
Quantity(kg) | Weight / m | length | No | Description | Item No.
 |  |  |  | Main Bars | 1
74.01 | 0.86 | 3.96 | 21 | a (st. bars φ12) | 
75.694 | 0.86 | 4.05 | 21 | b (bent. Bars φ12) | 
33.48 | 0.62 | 1.5 | 36 | c (add. Bars φ10) | 
 |  |  |  | Secondary Bars | 2
46.128 | 0.62 | 4.96 | 15 | c (st. bars φ10) | 
46.965 | 0.62 | 5.05 | 15 | d (bent. Bars φ10) | 
Φ12: ∑ ≈ 150kg
Φ10: ∑ ≈ 127kg
Note: tabulate the required amount of steel per each size separately as follows.
Following table represent the amount of steel for (S1).
Thus; total amount of steel required per each slab :
Φ12: ∑ ≈ 150kg
Φ10: ∑ ≈ 127kg
total amount of steel :
Φ12: ∑ ≈ 600kg
Φ10: ∑ ≈ 508kg

## Slide 15
Beam:
6- Reinforced Steel:
1
1
2
2
Section (1-1)
Section (2-2)
2Φ20
2Φ16
2Φ16 (1.75m)
2Φ20
5.1m
0.04cm
30
22
10cm
45
37
Φ10 @ 20cm c/c

## Slide 16
Bottom bars:
  Straight bars:
  length=5.1- (2*0.04) = 5.02
    Number of bars = 2
  Bent bars:
  length=(5.02)+0.84d
  = 3.96+0.84*0.37=5.33m
    Number of bars = 2
2 No. Φ20 with length of 5.02m
2 No. Φ20 with length of 5.33m
Top bars:
  Straight bars:
  Additional bars:
2 No. Φ16 with length of 5.02m
4 No. Φ16 with length of 1.75m
Stirrups:
Number of stirrups
length
26 No. Φ10 with length of 1.3m

## Slide 17
Quantity(kg) | Weight / m | length | No | Description | Item No.
 |  |  |  | Bottom bars | 1
24.79 | 2.47 | 5.02 | 2 | (st. bars φ20) | 
26.33 | 2.47 | 5.33 | 2 | (bent. Bars φ20) | 
 |  |  |  | Top bars | 2
15.86 | 1.58 | 5.02 | 2 | (st. bars φ16) | 
11.06 | 1.58 | 1.75 | 4 | (add. Bars φ16) | 
 |  |  |  | stirrups | 3
20.96 | 0.62 | 1.3 | 26 | φ10 | 
Φ20: ∑ ≈ 52kg
Φ10: ∑ ≈ 21kg
Φ16: ∑ ≈ 27kg

## Slide 18
3. Detailed Estimate:
Ex.: Estimate the quantities and cost of the following items of a two roomed building from the given plan and section in figure below.
Items:
Earth work in excavation at $1.0 per m3.
Crushed stone at $0.25 per m2.
Cement Concrete 1:2:4 in foundation at $40 per m3.
Brick work and cement mortar (1:3) in foundation at $50 per m3.
Brick work and cement mortar (1:3) in super structure (wall) at $80 per m3.
Aluminum window with all accessories at $100 per m2.
Steel door at $75 per m2.
Concrete floor at $35 per m3.
Reinforced concrete roof at $150 per m3.
Cement plastering at $3 per m2.
Gypsum plastering at $3 per m2.
Floor tile at $15 per m2.
Emulsion paint at $0.75 per m2.
Oil paint at $1.0 per m2.

## Slide 19
Plan and Section of 2 roomed building.

## Slide 20: Detail of measurements and calculation of quantities
Item No | Description | No | Length m | Width m | Height m | Unit | Quantity
1 | Excavation Long side Short side | 2 3 | 9.28 4.44 | 0.8 0.8 | 0.6 0.6 | m3 | 8.909 6.394
2 | Crushed stone Long side Short side | 2 3 | 9.28 4.44 | 0.8 0.8 | -- -- | m2 | 14.848 10.656
3 | Concrete 1:2:4 Long side Short side | 2 3 | 9.28 4.44 | 0.8 0.8 | 0.2 0.2 | m3 | 2.969 2.131
4 | Block work Long side Short side | 2 3 | 8.88 4.84 | 0.4 0.4 | 0.2 0.2 | m3 | 1.42 1.162
∑ = 15.302
∑= 25.504
∑= 5.101
∑= 2.582

## Slide 21
Item No | Description | No | Length m | Width m | Height m | Unit | Quantity
5 | Brick work (wall) Long side Short side Doors windows | 2 3 2 4 | 8.72 5.00 1.20 1.00 | 0.24 0.24 0.24 0.24 | 3 3 2.2 1.5 | m3 | 12.557 10.800 -1.267 -1.440
6 | Aluminum windows | 4 | 1.0 | -- | 1.5 | m2 | 6.0
7 | Steel doors | 2 | 1.2 | -- | 2.2 | m2 | 5.28
8 | Concrete floor 1:2:4 Room 1 Room 2 | 1 1 | 5.0 5.0 | 5.0 3.0 | 0.1 0.1 | m3 | 2.5 1.5
9 | Reinforced concrete slab | 1 | 9.72 | 6.48 | 0.15 | m3 | 9.448
10 | Cement plastering Front &back facing Sides facing Under slab projection Long side Short side | 2 2 2 2 | 8.72 5.48 9.72 5.48 | -- -- 0.5 0.5 | 3.0 3.0 -- -- | m2 | 52.32 32.88 9.72 5.48
∑ = 20.649
∑ = 4.0

## Slide 22
 | Facing of Slabs front &back: sides: Around doors Around windows Doors Windows | 2 2 4 2 8 8 2 4 | 9.72 6.48 -- 1.2 -- 1.0 1.2 1.0 | -- -- 0.07 0.07 0.07 0.07 -- -- | 0.15 0.15 2.2 -- 1.5 -- 2.2 1.5 |  | 2.916 1.944 0.616 0.168 0.84 0.56 -5.28 -6.00
11 | Gypsum plastering |  |  |  |  | m2 | 
 | Room1: Walls | 2 | -- | 3 | 2.85 |  | 17.1
 |  | 2 | 5 | -- | 2.85 |  | 28.4
 | ceiling | 1 | 5 | 3 | -- |  | 15
 | Room 2: walls | 4 | 5 | -- | 2.85 |  | 57
 | Ceiling Around doors Around shelves Doors Windows | 1 4 2 4 4 2 4 | 5 1.2 1 1.2 1.0 | 5 0.07 0.07 0.12 0.12 | -- 2.2 1.5 2.2 1.5 |  | 25 0.616 0.168 0.72 0.48 -5.28 -6.00
∑ = 96.164
∑ = 133.3

## Slide 23
Item No | Description | No | Length m | Width m | Height m | Unit | Quantity
12 | floor tile Room 1 Room 2 Under door | 1 1 2 | 5 5 1.2 | 3 5 0.24 | -- -- -- | m2 | 15 25 0.576
13 | Emulsion paint “on gypsum plastering” |  |  |  |  |  | 
14 | Oil paint |  |  |  |  | m2 | 
∑ = 41
∑ = 0
∑ = 133.3

## Slide 24
Sanitary and Water supply involves the following items:
Specifications and requirements | Unit | Item
Number of user, type of construction material, required plan and section….etc | no. | Septic tank
Depth, location, section…etc | no. | Pit Latrine
 | no | Pan or (WC)
 | no. | Urinal
Precast pipe thickness, slope, concrete line, section and diameter.. | m.l | CC pipe
Cast iron pipe diameter and mechanical specification. | m.l | CI pipe
Size, sectional detail of construction for large manholes. | no. | Manholes
Type of material | no. | Kitchen sink
Antibacterial or traditional | no. | Wash basin
 | no. | Flushing cistern
Specifications and requirements | Unit | Item
diameter | m.l | GI (Galvanized Iron Pipe)
 | no. | Valve
diameter | m.l | PPR-pipe
 | no. | Water Tanks
 | no. | Boilers